## Slide 1: RM2D
Let’s write our FIRST basic SPIN program!

## Slide 2: The Labs that follow in this Module are designed to teach the following;
Turn an LED on – assigning I/O pin direction and output state
Turn groups of LEDs on – group I/O assignments
Signal a pushbutton state with an LED – monitoring an input & setting an output
Signal a group of pushbutton states with LEDs – parallel I/O, monitoring a group of inputs and writing to a group of outputs
Synchronized LED on/off signals – event timing based on a register that counts clock ticks
Configure the Propeller chip’s system clock – choosing a clock source and configuring the Propeller chip’s Phase-Locked Loop (PLL) frequency multiplier
Display on/off patterns – Introduction to Spin operators commonly used on I/O registers
Display binary counts – introductions to several types of operators and conditional looping code block execution
Shift a light display – conditional code block execution and shift operations
Shift a light display with pushbutton-controlled refresh rate – global and local variables
and more conditional code block execution
Timekeeping application with binary LED display of seconds – Introduction to
synchronized event timing that can function independently of other tasks in a given cog.

## Slide 3: Propeller Terminology: Over the next few slides, definitions are given for terms used in this set of lab activities. It would be good to understand these terms as they are used frequently!
Cog – a processor inside the Propeller chip. The Propeller chip has eight cogs, making it possible to perform lots of tasks in parallel. The Propeller is like a super-microcontroller with eight high speed 32-bit processors inside. Each internal processor (cog) has access to the Propeller chip’s I/O pins and 32 KB of global RAM. Each cog also has its own 2 KB of RAM that can either run a Spin code interpreter or an assembly language program.

## Slide 4
Spin language – The Spin language is the high-level programming language created by Parallax for the Propeller chip. Cogs executing Spin code do so by loading a Spin interpreter from the Propeller chip’s ROM. This interpreter fetches and executes Spin command codes that get stored in the Propeller chip’s Global RAM.

## Slide 5
Propeller cogs can also be programmed in low-level assembly language. Whereas high-level Spin tells a cog what to do, low-level assembly language tells a cog how to do it. Assembly language generates machine codes that reside in a cog’s RAM and get executed directly by the cog.
Assembly language programs make it possible to write code that optimizes a cog’s performance; however, it requires a more in-depth understanding of the Propeller chip’s architecture. The PE Kit Fundamentals labs focus on Spin programming.

## Slide 6
Method – a block of executable Spin commands that has a name, access rule, and can optionally create local (temporary) variables, receive parameters, and return a value.

## Slide 7
Global and local variables – Global variables are available to all the methods in a given object, and they reserve variable space as long as an application is running. Local variables are defined in a method, can only be used within that method, and only exist while that method executes commands. When it’s done, the memory these local variables used becomes available to other methods and their local variables. Local and global variables are defined with different syntax.

## Slide 8
Object – an application building block comprised of all the code in a given .spin file. Some Propeller applications use just one object but most use several. Objects have a variety of uses, depending partially on how they are written and partially on how they get configured and used by other objects. Some objects serve as top objects, which provide the starting point where the first command in a given application gets executed. Other objects are written to provide a library of useful methods for top objects or other objects to use.

## Slide 9
Objects can be written to use just one cog, or can include code that gets launched into one or more additional cogs. Some objects have methods that provide a means to exchange information with processes running in other cogs. One object can even make multiple copies of another object, and set each one to a different task. Objects can use other objects, which in turn can use still other objects.
In more complex applications, a set of objects will form functional relationships that can be viewed as a file structure with the Propeller Tool’s Object Info window. The examples in this lab only involve single, top-level objects with just one method.
Upcoming labs will introduce various building-block techniques for using multiple objects and methods in an application, as well as parallel multiprocessing applications using multiple cogs. Though the objects in this lab are simple, many of them will be modified later to serve as building blocks for other objects and/or future projects.

## Slide 10: Lights on with Direction and Output Register Bits: The LedOnP20 object shown below has a method named LedOn, with commands that instruct a cog in the Propeller chip to set its P20 I/O pin to output-high. This in turn causes the LED in the circuit connected to P20 to emit light.
‘File: LedOnP20.Spin
PUB LedOn ‘Method declaration
dira[20] := 1 ‘Set P20 to output
outa[20] := 1 ‘Set P20 to high
repeat ‘Endless loop keeps program from ending.
Type the code below into the Propeller tool window.
Go to NEXT slide
Now Load LedOnP20 into RAM by clicking Run → Compile Current → Load RAM (or press the F10 key).
NOTE: You can also press the F11 key which loads the code into EEPROM and stores it for later use.

## Slide 11: So what happened?
Did an LED light up?
If so, Which One?
Why do you think that happened?